## Slide 1
promix-center.com
REMOTE CONTROL ELECTROMECHANICAL LOCK FOR SINGLE DOOR COMMERCIAL REFRIGERATORS

## Slide 2: Promix-FRS.1D.01
Universal electromechanical lock for single-door refrigerator (set)
promix-center.com

## Slide 3: SCOPE OF DELIVERY
1 – Promix-SM.131.10 lock 1 pc.
2 – Promix -AD.DB.13 deadbolt 1 pc.
3 – Promix -AD.BR.05 bracket 1 pc.
4 – Promix -AD.BR.06 bracket 1 pc.
5 – Promix -CR.RX.02 controller 1 pc.
6 – Promix-CR.TX.01 RCU 1 pc.
7 – 4х16 self-tapping screws
(with pressing disk) 8 pcs
8 – М4х6 screw (with pressing disk) 2 pcs
9 – Self-adhesive vinyl film (25 mm)
for disguise camouflage of wire. 1 m
10 – Operating manual 1 pc.
promix-center.com

## Slide 4: Remote control system via radio channel
promix-center.com
Built-in power supply with electronic short circuit and overload protection
Programming directly from the controller (jumpers) and remotely using a master key fob
Up to 10 keyfobs can be recorded in the controller's memory
Possibility of separate replacement of the power supply and radio module during repair

## Slide 5: Installing the lock on single-door refrigerators. Installation and connection.
Designed for installation on the most of single-door commercial refrigerators of different producers.
promix-center.com
Lock installation place
Installation places for the controller
Deadbolt installed
RECOMMENDED PLACES FOR INSTALLATIONS

## Slide 6: Depending on the type of door profile. To install
promix-center.com
Promix -AD.BR.05 bracket
Promix -AD.BR.06 bracket

## Slide 7: Deadbolt installation
promix-center.com
Install the Promix-AD.DB.13 deadbolt
on the installed bracket

## Slide 8: Lock installation
promix-center.com
Close the fridge door and press on it – the bolt will make a mark on the walls of the door; Drill a hole with a diameter of 24 mm in the center of the mark; Drill a hole with a diameter of 6 mm from inside the refrigerator;

## Slide 9: Lock installation
promix-center.com
Stretch the lock wire with a wire loop;
Secure the lock, lay the wire and seal it with decorative tape;

## Slide 10: Testing
promix-center.com
Check that the deadbolt easily enters the lock hole;

## Slide 11: Controller installation
promix-center.com
Install the controller behind the advertising panel or in the compressor compartment and connect to the 220V and to the lock;

## Slide 12: Controller connection diagram
promix-center.com
1 – setting of the Normally Open lock;
2 –setting of the Normally Closed lock;
3 –programming.
Controller
Key fob/RCU
Lock
220V
Antenna
Jumper positions

## Slide 13
promix-center.com
+7 (4812) 619-330
+7 (920) 317-18-47
mail@promix-center.com
dis@promix-center.com
Trusted by thousands of users!